## Slide 1
COMPUTER NETWORKS
Sivaraman Eswaran Ph.D.
Department of Computer Science and Engineering

## Slide 2
COMPUTER NETWORKS
Link Layer and LAN
Sivaraman Eswaran Ph.D.
Department of Computer Science and Engineering

## Slide 3
Introduction
Error detection, correction
Multiple access protocols
LANs
    addressing, ARP
    Ethernet
    switches
A day in the life of a web request
Physical layer
Wireless LANs: IEEE 802.11
COMPUTER NETWORKS
Unit – 5 Link Layer and LAN Roadmap

## Slide 4
Introduction
Error detection, correction
Multiple access protocols
LANs
    addressing, ARP
    Ethernet
    switches
A day in the life of a web request
Physical layer
Wireless LANs: IEEE 802.11
COMPUTER NETWORKS
Unit – 5 Link Layer and LAN Roadmap

## Slide 5
Introduction to Link layer
COMPUTER NETWORKS
link layer has responsibility of
transferring datagram from one node to physically adjacent node over a link
mobile network
enterprise
network
national or global ISP
datacenter
network
Terminology:
Hosts, routers, switches, WiFi access points: Nodes
communication channels that connect adjacent nodes along communication path: Links
  wired
  wireless
  LANs
layer-2 packet: frame, encapsulates datagram

## Slide 6
Datagram transferred by different link protocols over different links:
  e.g., WiFi on first link, Ethernet on next link
Each link protocol provides different services
  e.g., may or may not provide reliable data transfer over link
transportation analogy:
trip from Princeton to Lausanne
  limousine: Princeton to JFK airport
  plane: JFK to Geneva
  train: Geneva to Lausanne
tourist = datagram
transport segment = communication link
transportation mode = link-layer protocol
travel agent = routing algorithm
Link Layer: Context
COMPUTER NETWORKS

## Slide 7
…
…
Link Layer: Services
COMPUTER NETWORKS
framing, link access:
  encapsulate datagram into frame, adding header, trailer
  channel access if shared medium
  “MAC” addresses in frame headers identify source, destination (different from IP address!)
reliable delivery between adjacent nodes
  we already know how to do this!
  rarely used on low bit-error links (coax, fiber, etc)
  wireless links: high error rates

## Slide 8
…
…
Link Layer: Services
COMPUTER NETWORKS
flow control:
  pacing between adjacent sending and receiving nodes
error detection:
  errors caused by signal attenuation, noise.
  receiver detects errors, signals retransmission, or drops frame
error correction:
  receiver identifies and corrects bit error(s) without retransmission
half-duplex and full-duplex:
  with half duplex, nodes at both ends of link can transmit, but not at same time

## Slide 9
In each-and-every host
Link layer implemented in network interface card (NIC) or on a chip
  Ethernet, WiFi card or chip
  implements link, physical layer
Attaches into host’s system buses
Combination of hardware, software, firmware
Where is the link layer implemented?
COMPUTER NETWORKS
controller
physical
cpu
memory
host bus
(e.g., PCI)
network interface
application
transport
network
link
link
physical

## Slide 10
controller
physical
memory
CPU
controller
physical
cpu
memory
application
transport
network
link
link
physical
application
transport
network
link
link
physical
Sending side:
encapsulates datagram in frame
adds error checking bits, reliable data transfer, flow control, etc.
Receiving side:
looks for errors, reliable data transfer, flow control, etc.
extracts datagram, passes to upper layer at receiving side
linkh
linkh
datagram
datagram
datagram
Interfaces communicating
COMPUTER NETWORKS

## Slide 11
Introduction
Error detection, correction
Multiple access protocols
LANs
    addressing, ARP
    Ethernet
    switches
A day in the life of a web request
Physical layer
Wireless LANs: IEEE 802.11
COMPUTER NETWORKS
Unit – 5 Link Layer and LAN Roadmap

## Slide 12
EDC: error detection and correction bits (e.g., redundancy)
D: data protected by error checking, may include header fields
Error detection not 100% reliable!
  protocol may miss some errors, but rarely
  larger EDC field yields better detection and correction
datagram
D
EDC
d data bits
bit-error prone link
D’
EDC’
all
bits in D’
OK
?
N
detected
error
otherwise
datagram
COMPUTER NETWORKS
Error detection

## Slide 13
COMPUTER NETWORKS
Parity checking
single bit parity:
detect single bit errors
0111000110101011
1
parity
bit
d data bits
two-dimensional bit parity:
detect and correct single bit errors
d1,1
d2,1
di,1
. . .
d1,j+1
d2,j+1
di,j+1
. . .
. . .
d1,j
d2,j
di,j
. . .
di+1,1
di+1,j+1
di+1,j
. . .
. . .
. . .
. . .
row parity
column
parity
0 1 1 1 0 1
1 0 1 0 1 1
1 1 1 1 0 0
0 0 1 0 1 0
no errors:
0 1 1 1 0 1
1 0 1 0 1 1
1 0 1 1 0 0
1 0 1 0 1 0
parity
error
parity
error
detected
and
correctable
single-bit
error:
Even parity: set parity bit so there is an even number of 1’s

## Slide 14
COMPUTER NETWORKS
Two dimensional bit parity check - Example

## Slide 15
Sender:
treat contents of UDP segment (including UDP header fields and IP addresses) as sequence of 16-bit integers
checksum: addition (one’s complement sum) of segment content
checksum value put into UDP checksum field
Receiver:
compute checksum of received segment
check if computed checksum equals checksum field value:
  not equal - error detected
  equal - no error detected. But maybe errors nonetheless? More later ….
Goal: detect errors (i.e., flipped bits) in transmitted segment
COMPUTER NETWORKS
Internet checksum (review)

## Slide 16
COMPUTER NETWORKS
Two dimensional bit parity check - Example

## Slide 17
COMPUTER NETWORKS
Cyclic Redundancy Check (CRC Codes)
more powerful error-detection coding
D: data bits (given, think of these as a binary number)
G: bit pattern (generator), of r+1 bits (given)
goal: choose r CRC bits, R, such that <D,R> exactly divisible by G (mod 2)
  receiver knows G, divides <D,R> by G. If non-zero remainder: error detected!
  can detect all burst errors less than r+1 bits
  widely used in practice (Ethernet, 802.11 WiFi)
r CRC bits
d data bits
D
R
<D,R> = D 2r XOR R
*
bit pattern
formula for bit pattern

## Slide 18
COMPUTER NETWORKS
Sender Side – Calculation of CRC
A string of n 0’s is appended to the data unit to be transmitted.
Here, n is one less than the number of bits in CRC generator.
Binary division is performed of the resultant string with the CRC generator.
After division, the remainder so obtained is called as CRC.
It may be noted that CRC also consists of n bits.

## Slide 19
COMPUTER NETWORKS
Receiver Side – Check
The received code word is divided with the same CRC generator.
On division, the remainder so obtained is checked.
Case-1: Remainder = 0,
  No error
  Receiver accepts the data
Case-2: Remainder ≠ 0
  Receiver assumes that some error occurred
  Receiver rejects the data and asks the sender for retransmission.

## Slide 20
COMPUTER NETWORKS
CRC Generator
an algebraic polynomial represented as a bit pattern
Rule - The power of each term gives the position of the bit and the coefficient gives the value of the bit.
Consider the CRC generator is x7 + x6 + x4 + x3 + x + 1.

## Slide 21
COMPUTER NETWORKS
Cyclic Redundancy Check (CRC): Example
Calculation for the case of:
D = 101110, d = 6,
G = 1001, and r = 3.
1 0 0 1
1 0 1 0
1 0 1
0 0 0
1 0 0 1
1 0 0 1
1 0 0 1
0 0 0
1 1 0
1 1 0 0
1 0 1 0
0 1 1
0 1 1
D
R
1 0 0 1
G
0 0 0
1 0 1 1 1 0
2r
*
1
0
1

## Slide 22
COMPUTER NETWORKS
CRC – Numerical Example
A bit stream 1101011011 is transmitted using the standard CRC method. The generator polynomial is x4+x+1.
What is the actual bit string transmitted?
Solution
Generator polynomial G(x) = x4 + x + 1 is encoded as 10011.
G(x) consists of 5 bits. So, a string of 4 zeroes is appended to the bit stream to be transmitted.
The resulting bit stream is 11010110110000.

## Slide 23
COMPUTER NETWORKS
CRC – Numerical Example
A bit stream 10011101 is transmitted using the standard CRC method. The generator polynomial is x3+1.
  What is the actual bit string transmitted?
  Suppose the third bit from the left is inverted during transmission. How will receiver detect this error?
Solution
Generator polynomial G(x) = x3 + 1 is encoded as 1001.
G(x) consists of 4 bits. 4 zeroes is appended now.
The resulting bit stream is 10011101000.
Solution (Part-1)
Code word to be transmitted is obtained by replacing the last 3 zeroes of 10011101000 with the CRC.
Code word transmitted to the receiver = 10011101100.

## Slide 24
COMPUTER NETWORKS
CRC – Numerical Example
Solution (Part-2)
According to the question,
The bit stream received by the receiver = 10111101100.
Receiver performs the binary division with the same G(x).
Remainder obtained on division is a non-zero value.
Error occurred

## Slide 25
Introduction
Error detection, correction
Multiple access protocols
LANs
    addressing, ARP
    Ethernet
    switches
A day in the life of a web request
Physical layer
Wireless LANs: IEEE 802.11
COMPUTER NETWORKS
Unit – 5 Link Layer and LAN Roadmap

## Slide 26
COMPUTER NETWORKS
Multiple access links, Protocols
two types of “links”:
point-to-point
  point-to-point link between Ethernet switch, host
  PPP, HDLC
broadcast (shared wire or medium)
  old-fashioned Ethernet
  upstream HFC in cable-based access network
  802.11 wireless LAN, 4G/4G, satellite
shared wire (e.g.,
cabled Ethernet)
shared radio: WiFi
shared radio: satellite
humans at a cocktail party
(shared air, acoustical)
shared radio: 4G/5G

## Slide 27
Single shared broadcast channel
Two or more simultaneous transmissions by nodes: interference
  collision if node receives two or more signals at the same time
Distributed algorithm that determines how nodes share channel, i.e., determine when node can transmit
Communication about channel sharing must use channel itself!
  no out-of-band channel for coordination
Multiple access protocol
COMPUTER NETWORKS
Multiple access protocols

## Slide 28
Given: multiple access channel (MAC) of rate R bps
desiderata:
  1. when one node wants to transmit, it can send at rate R.
  2. when M nodes want to transmit, each can send at average rate R/M
  3. fully decentralized:
    no special node to coordinate transmissions
    no synchronization of clocks, slots
  4. simple
COMPUTER NETWORKS
An ideal Multiple access protocol

## Slide 29
Three broad classes:
channel partitioning (TDMA, FDMA, CDMA)
  divide channel into smaller “pieces” (time slots, frequency, code)
  allocate piece to node for exclusive use
random access (ALOHA, slotted ALOHA, CSMA, CSMA/CD, CSMA/CA
  channel not divided, allow collisions
  “recover” from collisions
“taking turns”
  nodes take turns, but nodes with more to send can take longer turns
COMPUTER NETWORKS
MAC protocols : Taxonomy
Included in the syllabus

## Slide 30
Simple CSMA: listen before transmit:
  if channel sensed idle: transmit entire frame
  if channel sensed busy: defer transmission
Human analogy: don’t interrupt others!
CSMA/CD: CSMA with collision detection
  collisions detected within short time
  colliding transmissions aborted, reducing channel wastage
  collision detection easy in wired, difficult with wireless
human analogy: the polite conversationalist
COMPUTER NETWORKS
CSMA (Carrier Sense Multiple Access)
Listen before speaking – Carrier Sensing
If someone else begins talking at the same time, stop talking – Collision Detection

## Slide 31
COMPUTER NETWORKS
CSMA Collisions
collisions can still occur with carrier sensing:
  propagation delay means two nodes may not hear each other’s just-started transmission
collision: entire packet transmission time wasted
  distance & propagation delay play role in in determining collision probability
spatial layout of nodes

## Slide 32
COMPUTER NETWORKS
CSMA/CD
CSMA/CS reduces the amount of time wasted in collisions
  transmission aborted on collision detection
spatial layout of nodes

## Slide 33
COMPUTER NETWORKS
Ethernet CSMA/CD Algorithm
NIC receives datagram from network layer, creates frame
If NIC senses channel:
  if idle: start frame transmission.
  if busy: wait until channel idle, then transmit
If NIC transmits entire frame without collision, NIC is done with frame!
If NIC detects another transmission while sending: abort, send jam signal
After aborting, NIC enters binary (exponential) backoff:
  after n collisions, NIC chooses K at random from {0,1,2, …, 2m-1}.
  NIC waits K·512 bit times, returns to Step 2
  more collisions: longer backoff interval

## Slide 34
COMPUTER NETWORKS
CSMA (Carrier Sense Multiple Access)
Tprop = max prop delay between 2 nodes in LAN
ttrans = time to transmit max-size frame
efficiency goes to 1
  as tprop goes to 0
  as ttrans goes to infinity
better performance than ALOHA: and simple, cheap, decentralized!

## Slide 35
Introduction
Error detection, correction
Multiple access protocols
Switched LANs
      LL addressing, ARP
    Ethernet
    switches
A day in the life of a web request
Physical layer
Wireless LANs: IEEE 802.11
COMPUTER NETWORKS
Unit – 5 Link Layer and LAN Roadmap

## Slide 36
32-bit IP address:
  network-layer address for interface
  used for layer 3 (network layer) forwarding
  e.g.: 128.119.40.136
MAC (or LAN or physical or Ethernet) address:
  function: used “locally” to get frame from one interface to another physically-connected interface (same subnet, in IP-addressing sense)
  48-bit MAC address (for most LANs) burned in NIC ROM, also sometimes software settable
hexadecimal (base 16) notation
(each “numeral” represents 4 bits)
  e.g.: 1A-2F-BB-76-09-AD
COMPUTER NETWORKS
MAC Addresses

## Slide 37
Each interface on LAN
has unique 48-bit MAC address
has a locally unique 32-bit IP address (as we’ve seen)
1A-2F-BB-76-09-AD
58-23-D7-FA-20-B0
0C-C4-11-6F-E3-98
71-65-F7-2B-08-53
LAN
(wired or wireless)
137.196.7/24
137.196.7.78
137.196.7.14
137.196.7.88
137.196.7.23
COMPUTER NETWORKS
MAC Addresses

## Slide 38
MAC address allocation administered by IEEE
manufacturer buys portion of MAC address space (to assure uniqueness)
analogy:
  MAC address: like Social Security Number
  IP address: like postal address
MAC flat address: portability
  can move interface from one LAN to another
  recall IP address not portable: depends on IP subnet to which node is attached
COMPUTER NETWORKS
MAC Addresses

## Slide 39
ARP table: each IP node (host, router) on LAN has table
Question: how to determine interface’s MAC address, knowing its IP address?
1A-2F-BB-76-09-AD
58-23-D7-FA-20-B0
0C-C4-11-6F-E3-98
71-65-F7-2B-08-53
LAN
137.196.7.78
137.196.7.14
137.196.7.88
137.196.7.23
ARP
ARP
ARP
ARP
  IP/MAC address mappings for some LAN nodes:
< IP address; MAC address; TTL>
  TTL (Time To Live): time after which address mapping will be forgotten (typically 20 min)
COMPUTER NETWORKS
ARP: Address Resolution Protocol

## Slide 40
58-23-D7-FA-20-B0
137.196.7.14
B
C
D
TTL
71-65-F7-2B-08-53
137.196.7.23
A
ARP table in A
IP addr
MAC addr
TTL
Example: A wants to send datagram to B
  B’s MAC address not in A’s ARP table, so A uses ARP to find B’s MAC address
A broadcasts ARP query, containing B's IP addr
  destination MAC address = FF-FF-FF-FF-FF-FF
  all nodes on LAN receive ARP query
1
Source MAC: 71-65-F7-2B-08-53
Source IP: 137.196.7.23
Target IP address: 137.196.7.14
…
1
Ethernet frame (sent to FF-FF-FF-FF-FF-FF)
COMPUTER NETWORKS
ARP Protocol in action

## Slide 41
58-23-D7-FA-20-B0
137.196.7.14
B
C
D
TTL
71-65-F7-2B-08-53
137.196.7.23
A
ARP table in A
IP addr
MAC addr
TTL
Example: A wants to send datagram to B
  B’s MAC address not in A’s ARP table, so A uses ARP to find B’s MAC address
B replies to A with ARP response, giving its MAC address
2
Target IP address: 137.196.7.14
Target MAC address:
58-23-D7-FA-20-B0
…
2
ARP message into Ethernet frame (sent to 71-65-F7-2B-08-53)
COMPUTER NETWORKS
ARP Protocol in action

## Slide 42
58-23-D7-FA-20-B0
137.196.7.14
B
C
D
TTL
71-65-F7-2B-08-53
137.196.7.23
A
ARP table in A
IP addr
MAC addr
TTL
Example: A wants to send datagram to B
  B’s MAC address not in A’s ARP table, so A uses ARP to find B’s MAC address
A receives B’s reply, adds B entry into its local ARP table
3
137.196.
7.14
58-23-D7-FA-20-B0
500
COMPUTER NETWORKS
ARP Protocol in action

## Slide 43
Walkthrough: sending a datagram from A to B via R
  Focus on addressing – at IP (datagram) and MAC layer (frame) levels
R
A
B
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
  Assume that:
    A knows B’s IP address
    A knows IP address of first hop router, R (how?)
    A knows R’s MAC address (how?)
COMPUTER NETWORKS
Routing to another Subnet : Addressing

## Slide 44
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
IP
Eth
Phy
IP src: 111.111.111.111
IP dest: 222.222.222.222
A creates IP datagram with IP source A, destination B
A creates link-layer frame containing A-to-B IP datagram
  R's MAC address is frame’s destination
MAC src: 74-29-9C-E8-FF-55
MAC dest: E6-E9-00-17-BB-4B
COMPUTER NETWORKS
Routing to another Subnet : Addressing

## Slide 45
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
IP
Eth
Phy
frame sent from A to R
IP
Eth
Phy
frame received at R, datagram removed, passed up to IP
MAC src: 74-29-9C-E8-FF-55
MAC dest: E6-E9-00-17-BB-4B
IP src: 111.111.111.111
IP dest: 222.222.222.222
IP src: 111.111.111.111
IP dest: 222.222.222.222
COMPUTER NETWORKS
Routing to another Subnet : Addressing

## Slide 46
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
IP src: 111.111.111.111
IP dest: 222.222.222.222
MAC src: 1A-23-F9-CD-06-9B
MAC dest: 49-BD-D2-C7-56-2A
R determines outgoing interface, passes datagram with IP source A, destination B to link layer
R creates link-layer frame containing A-to-B IP datagram. Frame destination address: B's MAC address
IP
Eth
Phy
COMPUTER NETWORKS
Routing to another Subnet : Addressing

## Slide 47
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
IP
Eth
Phy
IP
Eth
Phy
IP src: 111.111.111.111
IP dest: 222.222.222.222
MAC src: 1A-23-F9-CD-06-9B
MAC dest: 49-BD-D2-C7-56-2A
Transmits link-layer frame
R determines outgoing interface, passes datagram with IP source A, destination B to link layer
R creates link-layer frame containing A-to-B IP datagram. Frame destination address: B's MAC address
COMPUTER NETWORKS
Routing to another Subnet : Addressing

## Slide 48
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
IP
Eth
Phy
IP
Eth
Phy
B receives frame, extracts IP datagram destination B
B passes datagram up protocol stack to IP
IP src: 111.111.111.111
IP dest: 222.222.222.222
COMPUTER NETWORKS
Routing to another Subnet : Addressing

## Slide 49
Introduction
Error detection, correction
Multiple access protocols
Switched LANs
    LL addressing, ARP
      Ethernet
    switches
A day in the life of a web request
Physical layer
Wireless LANs: IEEE 802.11
COMPUTER NETWORKS
Unit – 5 Link Layer and LAN Roadmap

## Slide 50
COMPUTER NETWORKS
Ethernet
“dominant” wired LAN technology:
first widely used LAN technology
simpler, cheap
kept up with speed race: 10 Mbps – 400 Gbps
single chip, multiple speeds (e.g., Broadcom BCM5761)
Ethernet’ Success
  First widely deployed high-speed LAN
  Token ring, FDDI, and ATM were more complex and expensive than Ethernet
  Operated at equal data rates or higher.

## Slide 51
Bus: popular through mid 90s
  all nodes in same collision domain (can collide with each other)
bus: coaxial cable
switched
Switched: prevails today
  active link-layer 2 switch in center
  each “spoke” runs a (separate) Ethernet protocol (nodes do not collide with each other)
COMPUTER NETWORKS
Ethernet : Physical Topology

## Slide 52
Sending interface encapsulates IP datagram (or other network layer protocol packet) in Ethernet frame
dest.
address
source
address
data (payload)
CRC
preamble
type
Preamble:
Used to synchronize receiver, sender clock rates
7 bytes of 10101010 followed by one byte of 10101011
COMPUTER NETWORKS
Ethernet Frame Structure

## Slide 53
dest.
address
source
address
data (payload)
CRC
preamble
type
Addresses: 6 byte source, destination MAC addresses
  if adapter receives frame with matching destination address, or with broadcast address (e.g., ARP packet), it passes data in frame to network layer protocol
  otherwise, adapter discards frame
Type: indicates higher layer protocol
  mostly IP but others possible, e.g., Novell IPX, AppleTalk
  used to demultiplex up at receiver
CRC: cyclic redundancy check at receiver
  error detected: frame is dropped
COMPUTER NETWORKS
Ethernet Frame Structure ( more)

## Slide 54
Connectionless: no handshaking between sending and receiving NICs
Unreliable: receiving NIC doesn’t send ACKs or NAKs to sending NIC
  data in dropped frames recovered only if initial sender uses higher layer rdt (e.g., TCP), otherwise dropped data lost
Ethernet’s MAC protocol: unslotted CSMA/CD with binary backoff
COMPUTER NETWORKS
Ethernet : Unreliable Connectionless

## Slide 55
  Different physical layer media: fiber, cable
application
transport
network
link
physical
MAC protocol
and frame format
100BASE-TX
100BASE-T4
100BASE-FX
100BASE-T2
100BASE-SX
100BASE-BX
fiber physical layer
copper (twister pair) physical layer
Many different Ethernet standards
  Common MAC protocol and frame format
  Different speeds: 2 Mbps, 10 Mbps, 100 Mbps, 1Gbps, 10 Gbps, 40 Gbps
COMPUTER NETWORKS
802.3 Ethernet Standards: Link and Physical Layers

## Slide 56
Introduction
Error detection, correction
Multiple access protocols
Switched LANs
    Addressing, ARP
    Ethernet
    Switches
A day in the life of a web request
Physical layer
Wireless LANs: IEEE 802.11
COMPUTER NETWORKS
Unit – 5 Link Layer and LAN Roadmap

## Slide 57
Switch is a link-layer device: takes an active role
  Store, forward Ethernet frames
  Examine incoming frame’s MAC address, selectively forward frame to one-or-more outgoing links when frame is to be forwarded on segment, uses CSMA/CD to access segment
Transparent: hosts unaware of presence of switches
Plug-and-play, self-learning
  Switches do not need to be configured
COMPUTER NETWORKS
Ethernet switch

## Slide 58
switch with six interfaces (1,2,3,4,5,6)
A
A’
B
B’
C
C’
1
2
3
4
5
6
Hosts have dedicated, direct connection to switch
Switches buffer packets
Ethernet protocol used on each incoming link, so:
  no collisions; full duplex
  each link is its own collision domain
Switching: A-to-A’ and B-to-B’ can transmit simultaneously, without collisions
COMPUTER NETWORKS
Switch : Multiple Simultaneous Transmissions

## Slide 59
switch with six interfaces (1,2,3,4,5,6)
A
A’
B
B’
C
C’
1
2
3
4
5
6
Hosts have dedicated, direct connection to switch
Switches buffer packets
Ethernet protocol used on each incoming link, so:
  No collisions; full duplex
  Each link is its own collision domain
Switching: A-to-A’ and B-to-B’ can transmit simultaneously, without collisions
  but A-to-A’ and C to A’ can not happen simultaneously
COMPUTER NETWORKS
Switch: Multiple Simultaneous Transmissions

## Slide 60
A
A’
B
B’
C
C’
1
2
3
4
5
6
Q: How does switch know A’ reachable via interface 4, B’ reachable via interface 5?
A: Each switch has a switch table, each entry:
  (MAC address of host, interface to reach host, time stamp)
  looks like a routing table!
Q: How are entries created, maintained in switch table?
  something like a routing protocol?
COMPUTER NETWORKS
Switch Forwarding Table

## Slide 61
A
A’
B
B’
C
C’
1
2
3
4
5
6
Switch learns which hosts can be reached through which interfaces
A A’
Source: A
Dest: A’
MAC addr interface TTL
Switch table
(initially empty)
A
1
60
  When frame received, switch “learns” location of sender: incoming LAN segment
  Records sender/location pair in switch table
COMPUTER NETWORKS
Switch: Self-learning

## Slide 62
When frame received at switch:
  1. Record incoming link, MAC address of sending host
  2. Index switch table using MAC destination address
  3. If entry found for destination then {
  If destination on segment from which frame arrived then drop frame
  else forward frame on interface indicated by entry
  }
  else flood /* forward on all interfaces except arriving interface */
COMPUTER NETWORKS
Switch: Frame Filtering / Forwarding

## Slide 63
A
A’
B
B’
C
C’
1
2
3
4
5
6
A A’
Source: A
Dest: A’
MAC addr interface TTL
switch table
(initially empty)
A
1
60
A A’
A A’
A A’
A A’
A A’
A’ A
A’
4
60
Frame destination, A’, location unknown:
Flood
Destination A location known:
Selectively send on just one link
COMPUTER NETWORKS
Self-learning, Forwarding: Example

## Slide 64
Self-learning switches can be connected together:
Q: sending from A to G - how does S1 know to forward frame destined to G via S4 and S3?
A: self learning! (works exactly the same as in single-switch case!)
A
B
S1
C
D
E
F
S2
S4
S3
H
I
G
COMPUTER NETWORKS
Interconnecting Switches

## Slide 65
Suppose C sends frame to I, I responds to C
Q: show switch tables and packet forwarding in S1, S2, S3, S4
A
B
S1
C
D
E
F
S2
S4
S3
H
I
G
COMPUTER NETWORKS
Self-learning Multi-switch Example
Switch 1 | 
Address | Port
C | 1
I | 4
Switch 4 | 
Address | Port
C | 1
I | 3
Switch 2 | 
Address | Port
C | 4
Switch 3 | 
Address | Port
C | 4
I | 3

## Slide 66
to external
network
router
IP subnet
mail server
web server
COMPUTER NETWORKS
Small Institutional Network

## Slide 67
application
transport
network
link
physical
network
link
physical
link
physical
switch
datagram
application
transport
network
link
physical
frame
frame
frame
datagram
Both are store-and-forward:
Routers: network-layer devices (examine network-layer headers)
Switches: link-layer devices (examine link-layer headers)
Both have forwarding tables:
Routers: compute tables using routing algorithms, IP addresses
Switches: learn forwarding table using flooding, learning, MAC addresses
COMPUTER NETWORKS
Switches Vs Routers

## Slide 68
Introduction
Error detection, correction
Multiple access protocols
Switched LANs
      addressing, ARP
      Ethernet
      switches
A day in the life of a web request
Physical layer
Wireless LANs: IEEE 802.11
COMPUTER NETWORKS
Unit – 5 Link Layer and LAN Roadmap

## Slide 69
Our journey down the protocol stack is now complete!
  application, transport, network, link
Putting-it-all-together: synthesis!
  Goal: identify, review, understand protocols (at all layers) involved in seemingly simple scenario: requesting www page
  Scenario: student attaches laptop to campus network, requests/receives www.google.com
COMPUTER NETWORKS
Synthesis : A day in the life of a web request

## Slide 70
Comcast network
68.80.0.0/13
Google’s network
64.233.160.0/19
64.233.169.105
web server
DNS server
school network
68.80.2.0/24
browser
web page
Arriving mobile client attaches to network …
Requests web page: www.google.com
Scenario:
Sounds
simple!
COMPUTER NETWORKS
A day in the life of a web request

## Slide 71
router has
DHCP server
arriving mobile:
DHCP client
Connecting laptop needs to get its own IP address, addr of first-hop router, addr of DNS server: use DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP request encapsulated in UDP, encapsulated in IP, encapsulated in 802.3 Ethernet
Ethernet frame broadcast (dest: FFFFFFFFFFFF) on LAN, received at router running DHCP server
Ethernet demuxed to IP demuxed, UDP demuxed to DHCP
COMPUTER NETWORKS
A day in the life of a web request

## Slide 72
router has
DHCP server
arriving mobile:
DHCP client
DHCP
UDP
IP
Eth
Phy
DHCP
UDP
IP
Eth
Phy
DHCP server formulates DHCP ACK containing client’s IP address, IP address of first-hop router for client, name & IP address of DNS server
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP
Encapsulation at DHCP server, frame forwarded (switch learning) through LAN, demultiplexing at client
Client now has IP address, knows name & addr of DNS
server, IP address of its first-hop router
DHCP client receives DHCP ACK reply
COMPUTER NETWORKS
A day in the life : Connecting to the Internet

## Slide 73
router has
ARP server
arriving mobile:
ARP client
DNS
UDP
IP
Eth
Phy
Eth
Phy
ARP
Before sending HTTP request, need IP address of www.google.com: DNS
DNS
DNS
DNS
DNS query created, encapsulated in UDP, encapsulated in IP, encapsulated in Eth. To send frame to router, need MAC address of router interface: ARP
ARP query broadcast, received by router, which replies with ARP reply giving MAC address of router interface
Client now knows MAC address of first hop router, so can now send frame containing DNS query
ARP query
ARP
ARP reply
COMPUTER NETWORKS
A day in the life…. ARP (Before DNS, Before HTTP)

## Slide 74
DNS
UDP
IP
Eth
Phy
DNS
DNS
DNS
Comcast network
68.80.0.0/13
DNS
server
DNS
DNS
DNS
DNS
DNS
IP datagram containing DNS query forwarded via LAN switch from client to 1st hop router
IP datagram forwarded from campus network into Comcast network, routed (tables created by RIP, OSPF, IS-IS and/or BGP routing protocols) to DNS server
Demuxed to DNS
DNS replies to client with IP address of www.google.com
DNS
UDP
IP
Eth
Phy
DNS
DNS
DNS
DNS
DNS
COMPUTER NETWORKS
A day in the life…. Using DNS

## Slide 75
DNS
DNS
DNS
Comcast network
68.80.0.0/13
64.233.169.105
Google web server
HTTP
TCP
IP
Eth
Phy
HTTP
To send HTTP request, client first opens TCP socket to web server
TCP SYN segment (step 1 in TCP 3-way handshake) inter-domain routed to web server
TCP connection established!
SYN
SYN
SYN
SYN
TCP
IP
Eth
Phy
SYN
SYN
SYN
SYNACK
SYNACK
SYNACK
SYNACK
SYNACK
SYNACK
SYNACK
Web server responds with TCP SYNACK (step 2 in TCP 3-way handshake)
COMPUTER NETWORKS
A day in the life…. TCP Connection carrying HTTP

## Slide 76
DNS
DNS
DNS
Comcast network
68.80.0.0/13
64.233.169.105
Google web server
HTTP
TCP
IP
Eth
Phy
HTTP
TCP
IP
Eth
Phy
HTTP
HTTP request sent into TCP socket
IP datagram containing HTTP request routed to www.google.com
IP datagram containing HTTP reply routed back to client
Web server responds with HTTP reply (containing web page)
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
web page finally (!!!) displayed
COMPUTER NETWORKS
A day in the life…. HTTP Request / Reply

## Slide 77
Introduction
Error detection, correction
Multiple access protocols
Switched LANs
      addressing, ARP
      Ethernet
      switches
A day in the life of a web request
Physical layer
Wireless LANs: IEEE 802.11
COMPUTER NETWORKS
Unit – 5 Link Layer and LAN Roadmap

## Slide 78
COMPUTER NETWORKS
Physical Layer – OSI Reference Model
Implemented in Hardware
Implemented in Software

## Slide 79
COMPUTER NETWORKS
Purpose of Physical Layer

## Slide 80
COMPUTER NETWORKS
Physical Layer Services
The role of Physical Layer is to:
  encode the binary digits that represent data link layer frames into signals
  to transmit and receive these signals cross the physical media
    copper wires, optical fiber, and wireless that connect network devices.
  Physical medium - conduct a signal in the form of voltage, light, or radio waves from one device to another.
Analog signal – continuous-valued (amplitudes, frequencies)
Digital signal – discrete-valued (0s & 1s)

## Slide 81
COMPUTER NETWORKS
Physical Layer Services
  The delivery of frames across the local media requires the following physical layer elements:
    The physical media and associated connectors
    A representation of bits on the media
    Encoding of data and control information
    Transmitter and receiver circuitry on the network devices
Components to understand Physical Layer functions includes:
    Physical components
    Encoding
    Signaling
Physical Layer Devices
Hub
Repeater
Modem
Cables
Network Adapters

## Slide 82
COMPUTER NETWORKS
Physical Layer Services
Physical Layer Encoding

## Slide 83
COMPUTER NETWORKS
Physical Layer – Human Analogy
A person wants to communicate an idea:
processes an abstract thought into words (signaling) ->
encoded into speech sounds (encoding) ->
sent out through the medium of air (physical).
At the other end:
the receiver interprets the signal of sound,
recognizes patterns in the sound that denote words &
then processes the meaning of the words into the original idea

## Slide 84
COMPUTER NETWORKS
Physical Layer Principles

## Slide 85
COMPUTER NETWORKS
Signalling Bits for the Media

## Slide 86
COMPUTER NETWORKS
Signalling Methods
NRZ (Non Return to Zero) Encoding – A low voltage being 0 and a higher voltage representing a 1.
Manchester Encoding
A voltage change from low to high within the bit time represents a 1.
A voltage drop within the bit time from a high to a low voltage represents a 0.

## Slide 87
COMPUTER NETWORKS
Physical Layer – Signalling and Encoding

## Slide 88
COMPUTER NETWORKS
Physical Layer Standards
Some of the key organizations:
  The International Organization for Standardization (ISO)
  The Institute of Electrical and Electronics Engineers (IEEE)
  The American National Standards Institute (ANSI)
  The International Telecommunication Union (ITU)
  The Electronics Industry Alliance/Telecommunications Industry Association (EIA/TIA)
  National telecommunications authorities such as the Federal Communications Commission (FCC) in the United States

## Slide 89
COMPUTER NETWORKS
Transmission Media
core
cladding
jacket
light

## Slide 90
COMPUTER NETWORKS
Types of Physical Transmission Media

## Slide 91
Introduction
Error detection, correction
Multiple access protocols
Switched LANs
      addressing, ARP
      Ethernet
      switches
A day in the life of a web request
Physical layer
Wireless LANs: IEEE 802.11
COMPUTER NETWORKS
Unit – 5 Link Layer and LAN Roadmap

## Slide 92
COMPUTER NETWORKS
Elements of a Wireless Network
wired network
infrastructure

## Slide 93
COMPUTER NETWORKS
Elements of a Wireless Network
wired network
infrastructure
wireless hosts
laptop, smartphone, IoT
run applications
may be stationary (non-mobile) or mobile
  wireless does not always mean mobility!

## Slide 94
COMPUTER NETWORKS
Elements of a Wireless Network
wired network
infrastructure
base station
typically connected to wired network
relay - responsible for sending packets between wired network and wireless host(s) in its “area”
  e.g., cell towers, 802.11 access points

## Slide 95
COMPUTER NETWORKS
Elements of a Wireless Network
wired network
infrastructure
wireless link
typically used to connect mobile(s) to base station, also used as backbone link
multiple access protocol coordinates link access
various transmission rates and distances, frequency bands

## Slide 96
COMPUTER NETWORKS
Characteristics of Selected Wireless Links
Indoor
Outdoor
Midrange
outdoor
Long range
outdoor
10-30m
50-200m
200m-4Km
4Km-15Km
2 Mbps
4G LTE
802.11ac
802.11n
802.11g
802.11b
3.5 Gbps
600 Mbps
54 Mbps
11 Mbps
Bluetooth
802.11ax
14 Gbps
5G
10 Gbps
802.11 af,ah
2 Key Areas:
Coverage area &
Link rate

## Slide 97
COMPUTER NETWORKS
Elements of a Wireless Network
wired network
infrastructure
infrastructure mode
base station connects mobiles into wired network
handoff: mobile changes base station providing connection into wired network

## Slide 98
COMPUTER NETWORKS
ad hoc mode
no base stations
nodes can only transmit to other nodes within link coverage
nodes organize themselves into a network: routing, address assignment, DNS-like name translation, and more.
Elements of a Wireless Network

## Slide 99
COMPUTER NETWORKS
Wireless network taxonomy
single hop
multiple hops
infrastructure
(e.g., APs)
infrastructure less
host connects to base station (WiFi, cellular) which connects to larger Internet. Eg: 4G LTE
no base station, no connection to larger Internet.
eg: Bluetooth, ad hoc nets
host may have to relay through several wireless nodes to connect to larger
Internet: mesh net
no base station, no connection to larger Internet. May have to relay to reach other.
eg: MANET, VANET

## Slide 100
COMPUTER NETWORKS
IEEE 802.11 Wireless LAN (WiFi)
IEEE 802.11 standard | Year | Max data rate | Range | Frequency
802.11b | 1999 | 11 Mbps | 30 m | 2.4 Ghz
802.11g | 2003 | 54 Mbps | 30m | 2.4 Ghz
802.11n (WiFi 4) | 2009 | 600 | 70m | 2.4, 5 Ghz
802.11ac (WiFi 5) | 2013 | 3.47Gpbs | 70m | 5 Ghz
802.11ax (WiFi 6) | 2020 (exp.) | 14 Gbps | 70m | 2.4, 5 Ghz
802.11af | 2014 | 35 – 560 Mbps | 1 Km | unused TV bands (54-790 MHz)
802.11ah | 2017 | 347Mbps | 1 Km | 900 Mhz
all use CSMA/CA for multiple access, and have base-station and ad-hoc network versions

## Slide 101
COMPUTER NETWORKS
The 802.11 LAN architecture
wireless host communicates with base station
  base station = access point (AP)
Basic Service Set (BSS) (aka “cell”) in infrastructure mode contains:
  wireless hosts
  access point (AP): base station
  ad hoc mode: hosts only
BSS 1
BSS 2
Internet
switch
or router

## Slide 102
COMPUTER NETWORKS
802.11: Channels, Association
spectrum divided into channels at different frequencies
  AP assigns Service Set ID (SSID)
  AP admin chooses frequency for AP (2.4 GHz to 2.4835 GHz)
  interference possible: channel can be same as that chosen by neighboring AP! – WiFi Jungle
arriving host: must associate with an AP
  scans channels, listening for beacon frames containing AP’s name (SSID) and MAC address
  selects AP to associate with
  then may perform authentication
  then typically run DHCP to get IP address in AP’s subnet
BSS

## Slide 103
COMPUTER NETWORKS
802.11 active/passive scanning
AP 2
AP 1
H1
BBS 2
BBS 1
1
2
3
1
passive scanning:
beacon frames sent from APs
association Request frame sent: H1 to selected AP
association Response frame sent from selected AP to H1
AP 2
AP 1
H1
BBS 2
BBS 1
1
2
2
3
4
active scanning:
Probe Request frame broadcast from H1
Probe Response frames sent from APs
Association Request frame sent: H1 to selected AP
Association Response frame sent from selected AP to H1

## Slide 104
COMPUTER NETWORKS
IEEE 802.11: multiple access
avoid collisions: 2+ nodes transmitting at same time
802.11: CSMA - sense before transmitting
  don’t collide with detected ongoing transmission by another node
802.11: no collision detection!
  difficult to sense collisions: high transmitting signal, weak received signal due to fading
  can’t sense all collisions in any case: hidden terminal, fading
  goal: avoid collisions: CSMA/CollisionAvoidance
space
A
B
C
A
B
C
A’s signal
strength
C’s signal
strength
802.11’s link-layer acknowledgment scheme!!!

## Slide 105
COMPUTER NETWORKS
IEEE 802.11 MAC Protocol: CSMA/CA
802.11 sender
1 if sense channel idle for DIFS then
  transmit entire frame (no CD)
sender
receiver
DIFS
data
SIFS
ACK
802.11 receiver
if frame received OK
return ACK after SIFS (ACK needed due to hidden terminal problem)
2 if sense channel busy then
  start random backoff time
  timer counts down while channel idle
  transmit when timer expires
  if no ACK, increase random backoff interval, repeat 2
Short Inter-frame Spacing (SIFS)
Distributed Inter-frame Space (DIFS);

## Slide 106
COMPUTER NETWORKS
Avoiding Collisions (more)
idea: sender “reserves” channel use for data frames using small reservation packets
sender first transmits small request-to-send (RTS) packet to BS using CSMA
  RTSs may still collide with each other (but they’re short)
BS broadcasts clear-to-send CTS in response to RTS
CTS heard by all nodes
  sender transmits data frame
  other stations defer transmissions

## Slide 107
COMPUTER NETWORKS
Collision Avoidance: RTS-CTS exchange
AP
A
B
RTS(A)
RTS(B)
RTS(A)
CTS(A)
CTS(A)
DATA (A)
ACK(A)
ACK(A)
reservation collision
defer
time

## Slide 108
COMPUTER NETWORKS
802.11 frame: addressing
2
2
6
6
6
2
6
0 - 2312
4
Address 1: MAC address of wireless host or AP to receive this frame
Address 4: used only in ad hoc mode
frame
control
duration
address
1
address
2
address
4
address
3
payload
CRC
seq
control
Address 2: MAC address
of wireless host or AP
transmitting this frame
Address 3: MAC address of router interface to which AP is attached

## Slide 109
COMPUTER NETWORKS
802.11 frame: addressing
Internet
H1
R1
AP MAC addr
address 1
address 2
address 3
802.11 WiFi frame
R1 MAC addr
H1 MAC addr
R1 MAC addr
MAC dest addr
MAC source addr
802.3 Ethernet frame
H2 MAC addr

## Slide 110
COMPUTER NETWORKS
802.11 frame: addressing
2
2
6
6
6
2
6
0 - 2312
4
frame
control
duration
address
1
address
2
address
4
address
3
payload
CRC
seq
control
duration of reserved
transmission time (RTS/CTS)
frame sequence # (for reliable data transfer)
2
2
4
1
1
1
1
1
1
1
1
type
from
AP
subtype
to
AP
more
frag
WEP
more
data
power
mgt
retry
rsvd
protocol
version
frame type (RTS, CTS, ACK, data)

## Slide 111
COMPUTER NETWORKS
802.11: mobility within same subnet
H1 remains in same IP subnet: IP address can remain same
H1
BBS 2
BBS 1
switch: which AP is associated with H1?
  self-learning (Ch. 6): switch will see frame from H1 and “remember” which switch port can be used to reach H1

## Slide 112
COMPUTER NETWORKS
Suggested Readings

## Slide 113
sivaramane@pes.edu
+91 80 6666 3333 Extn 834
THANK YOU
Sivaraman Eswaran Ph.D.
Department of Computer Science and Engineering